## Slide 1: MIPS Single-Cycle Implementation
Pavel Kryukov
14 November 2015

## Slide 2: Layers of Abstraction in Computer Science (CS)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topic of this and next lectures

## Slide 3: Refresher: MIPS ISA
Register-to-register arithmetic instructions are R-type
Load, store, branch, & immediate instructions are I-type
The jump instruction uses the J-type instruction format
Moving data to/from memory uses imm($rs) for the effective address, ea = imm + $rs, to reference Mem[ea]
Branch and Jump destinations refer to words (instructions) not bytes
Branch offsets are relative to PC+4
op
rs
rt
rd
shamt
funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
op
rs
rt
imm
6 bits
5 bits
5 bits
16 bits
op
offset in words
6 bits
26 bits

## Slide 4: Single-Cycle Implementation of MIPS
Any ISA can be implemented in many different ways
The simplest one is single-cycle implementation:
  All operations are executed strongly sequentially
  Execution of an instruction is not started until the previous one is completely executed (no overlapping)
  All instructions take the same amount of time – a single cycle
For simplicity, only the following instructions will be considered
Arithmetic | add, sub, or, and, addi, subi
Data transfer | lw, sw
Control | beq

## Slide 5: Computer as a State Machine
A computer is just a big fancy state machine
  Registers, memory, hard disks and other storage form the state
  The processor keeps reading and updating the state, according to the instructions in some program
State
CPU

## Slide 6: Instruction Execution Cycle
Fetch Instruction by PC
Read registers
Process Calculations
Read/Write
Memory
Write registers
Update PC
Download instruction from the memory using value stored in the program counter (PC) register as an address.
Read values of registers which are pointed by the instruction as their source operands.
Execute an action encoded in the instruction (e.g. addition, subtraction, address calculation, etc.).
Write the result of the calculation into the memory or read the value using the address calculated on the previous step.
Write the result of the calculation or the value read on the previous step into the memory.
Update the program counter to the next instruction:
PC = PC + InstructionLength
Or it is a taken branch then:
PC = PC + InstructionLength + BranchOffset

## Slide 7: Instruction Fetch
The CPU is always in an infinite loop, fetching instructions from memory and executing them
The program counter or PC register holds the address of the current instruction
MIPS instructions are each four bytes long, so the PC should be incremented by four to read the next instruction in sequence
Add
4
Read
address
Instruction [31-0]
Memory
PC

## Slide 8: Executing R-Type Arithmetic Instructions
op
26
31
Read an instruction from the instruction memory by the address in PC
The source registers, specified by instruction fields rs and rt, should be read from the register file
The ALU performs the desired operation
Its result is stored in the destination register, which is specified by field rd of the instruction word
funct
0
5
shamt
6
10
rd
11
15
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [25-21]
I [20-16]
I [15-11]
ALUop
16
20
rt
rs
21
25

## Slide 9: Executing I-type Arithmetic Instructions
I [20-16]
I [15-11]
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [25-21]
ALUop
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
I [25-21]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
ALUSrc
R-type
26
31
0
5
6
10
11
15
16
20
op
funct
shamt
rd
rt
rs
21
25
op
imm
rt
rs
I-type
Read an instruction from the instruction memory by the address in PC
The 1st source register, specified by instruction field rs, should be read from the register file
The signed immediate is extended (from 16 to 32 bits) and directly transferred to ALU
The ALU performs the desired operation
Its result is stored in the destination register, which is specified by field rt of the instruction word
0
1
m
u
x
I [20-16]
I [15-11]
RegDst
Write
register

## Slide 10: Executing I-type Store Instructions
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
ALUSrc
RegDst
Read an instruction from the instruction memory by the address in PC
The 1st source register (base address), instruction field rs, is read from the register file
The 2nd source register (written value), instruction filed rt, is read from the register file
The signed displacement is extended (from 16 to 32 bits) and directly transferred to ALU
The ALU calculates the effective address
The value is written into the memory by the effective address
R-type
26
31
0
5
6
10
11
15
16
20
op
funct
shamt
rd
rt
rs
21
25
op
displ
rt
rs
I-type
Memory
Write
address
MemWrite
Write
data

## Slide 11: Executing I-type Load Instructions
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Memory
Write
address
Write
data
ALUSrc
MemWrite
RegDst
Read an instruction from the instruction memory by the address in PC
The 1st source register (base address), instruction field rs, is read from the register file
The signed displacement is extended (from 16 to 32 bits) and directly transferred to ALU
The ALU calculates the effective address
The value is read from the memory by the effective address
The result is written in the destination register specified by field rt
R-type
26
31
0
5
6
10
11
15
16
20
op
funct
shamt
rd
rt
rs
21
25
op
displ
rt
rs
I-type
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Memory
Write
address
Write
data
Read
address
ALUSrc
MemWrite
RegDst
Read
data
1
0
m
u
x
MemToReg

## Slide 12: Executing I-type Branch Instructions (1)
Read an instruction from the instruction memory by the address in PC
The source registers, specified by fields rs and rt, are be read from the register file
The signed offset is extended (from 16 to 32 bits) and shifted left by 2 (converted from words to bytes)
The address of the instruction after the branch is calculated (= PC + 4)
The target address of the branch is calculated as ((PC + 4) + (offset << 2))
The ALU compares the source operands (does subtraction) and generate the condition code (==, >, <, etc.)
The PC is update by the address of the instruction after the branch or by the target address depending on the branch opcode and the condition code
beq $t1, $t2, -0x0040
PC =
condition
target address
address of the next instruction
? ((PC + 4) + (-0x0040 << 2))
: (PC + 4)
((Reg[$t1] – Reg[$t2]) == 0)
depends on the branch opcode

## Slide 13: Executing I-type Branch Instructions (2)
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
Zero
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 2
ALUSrc
MemWrite
RegDst
MemToReg
0
1
m
u
x
PCSrc
Add
PC
4
Add
R-type
26
31
0
5
6
10
11
15
16
20
op
funct
shamt
rd
rt
rs
21
25
op
offset
rt
rs
I-type
The branch may or may not be taken, depending on the ALU’s Condition Code output (Zero here)

## Slide 14: The Final Single-Cycle Data Path
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
Zero
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 2
Add
Add
PC
4
0
1
m
u
x
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg

## Slide 15: Control Unit
The control unit is responsible for setting all the control signals so that each instruction is executed properly
The control unit needs 12 bits of an instruction
  Six bits make up the instruction opcode
  Six bits come from the instruction func field
It also needs the Conditional Code (“Zero”) output of the ALU
The control unit generates 7 of output, corresponding to the signals mentioned on the data path
Read
address
Instruction [31-0]
Memory
Read
address
Instruction [31-0]
Memory
RegWrite
ALUop
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
Control
I [31-26]
I [5-0]
CondCode

## Slide 16: Control signal table
sw and beq are the only instructions that do not write any registers
lw and sw are the only instructions that use the constant field. They also depend on the ALU to compute the effective memory address
ALUOp depends on the instructions’ func field
The PCSrc control signal shows if instruction is branch and it is taken
Operation | RegDst | RegWrite | ALUSrc | ALUOp | MemWrite | MemToReg | PCSrc
add | 1 | 1 | 0 | 010 | 0 | 0 | 0
sub | 1 | 1 | 0 | 110 | 0 | 0 | 0
addi | 0 | 1 | 1 | 010 | 0 | 0 | 0
subi | 0 | 1 | 1 | 110 | 0 | 0 | 0
or | 1 | 1 | 0 | 001 | 0 | 0 | 0
lw | 0 | 1 | 1 | 010 | 0 | 1 | 0
sw | X | 0 | 1 | 010 | 1 | X | 0
beq | X | 0 | 0 | 110 | 0 | X | 0/1

## Slide 17: Summary
A datapath contains all the functional units and connections necessary to implement an instruction set architecture.
  For our single-cycle implementation, we use two-ported memory, register file, an ALU, some extra adders, and lots of multiplexers.
  MIPS is a 32-bit machine, so most of the buses are 32-bits wide
The control unit tells the datapath what to do, based on the instruction that’s currently being executed
  The discussed processor has seven control signals that regulate the datapath
  The control signals can be generated by a combinational circuit with the instruction’s opcode and func fields as the input

## Slide 18: Acknowledgements
These slides contain material developed and copyright by:
Luis Ceze (UW), CS378, L1, L6 and L8

## Slide 19: Thank You Q/A