## Slide 1: Instruction Set Architecture (ISA)
Alexander Titov
10/20/2012

## Slide 2: What is Computer Architecture?
Computer architecture is the design of the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies.
Application
Physics
Decision: create many layers with standardized interfaces
Issue: the gap is too large to bridge it in one step

## Slide 3: Layers of Abstraction
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Hardware (HW)
Software (SW)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Interface between HW and SW

## Slide 4: ISA and uArch
Instruction Set Architecture (ISA) is a precise definition of computer’s instructions and their effects.
It can be thought as an agreement between a programmer and an engineer:
    It’s all programmer needs to program machine.
    It’s all hardware designer needs to design machine.
Microarchitecture (uArch, implementation) is an organization and features of Hardware that executes instructions defined by the ISA.

## Slide 5: ISA and uArch
What a typical ISA defines
    Data Formats. (Integer, Floating Point, Vector/Packed)
    Instructions. (Operations, encoding, etc.)
    Registers and Memory Organization.
    Interrupts, exceptions, and traps.
    Implementation-Dependent Features. (Memory control, custom features.)
What a typical uArch defines (not included into ISA)
    Memory hierarchy organization (caches, buses, etc.)
    Pipeline (forwarding, branch prediction, etc.)
    Out-of-order executions … and so on.
the programmer-visible state
they change the state

## Slide 6: Example of ISA and their uArches: MIPS
An example of a RISC processor.
    Designed for easy programming and implementation.
    Short and simple, but fast instructions → programs are larger than others, but run faster.
The main aim was to take advantages of pipelined execution
    Pipeline was not specified in ISA, but ISA developers tried to simplify its implementation in uArch.
Implementations:
    The first one is R2000 (1986)
    Later: R3000A (PlayStation), R4000 (PSP), R5900 (PlayStation 2), etc.
    Currently it is widely used in embedded systems.
One moment MIPS seemed to be overcome Intel IA-32, but it didn’t happen because Intel’s uArch was significantly better and could compensate the drawback of IA-32.
One moment MIPS seemed to be overcome Intel IA-32,, but it didn’t happen because Intel’s uArch was significantly better and could compensate the drawback of IA-32.

## Slide 7: Data Formats
In the memory all including data and program code is presented as binary numbers:
Data representation:
    Sizes: 8-b Bytes, 16-b Half words, 32-b words and 64-b double words (not used in our project)
    Formats: signed/unsigned integer, signed/unsigned floating point (not used in our project)
0000 0010 | 0011 0010 | 0100 0000 | 0010 0000
add $t0, $s1, $s2
0x2012620
=
=

## Slide 8: Memory addressing
Memory (MEM) is a concept of a storage for programs and their data
    It is a part of programmer-visible machine state (controlled by a programmer)
    It can be though as an linear array of Bytes.
    Data can be read or written into this storage using an index which is called memory address.
    The size of the memory is equal to Bytes, where N is the maximal number of bits that can be encoded in a memory address.
    There is no separate memory for code or data. They are stored together in the same space.
00100100
…
…
…
…
…
…
8 bits = 1 Byte
0
1
2

## Slide 9: Big and Little Endian
  Historically numbers are being written from the right to the left (the most significant digit is on the right):
  However, we used to enumerate elements in an array (and most other things) from the left to the right:
  The question: if we put an value of two bytes (e.g. 256) at the beginning of the array where the most significant byte will be? In element 0 or element 1?
Decimal 537 = 7* + 3* + 5*
Binary 1101 = 1* + 0* + 1* + 1*
…
…
…
…
…
…
…
0
1
2
Decimal 537 = 7* + 3* + 5*
Binary 1101 = 1* + 0* + 1* + 1*

## Slide 10: Big and Little Endian
  The answer: it depends on the ending which is defined in the ISA.
Decimal 256 = Binary 0000 0001 | 0000 0000
Bib Endian
Little Endian
15
8
7
0
Decimal 256 = Binary 0000 0001 | 0000 0000
Decimal 256 = Binary 0000 0001 | 0000 0000
Most significant byte
Least significant byte
0
1
2
00000001
00000000
7
0
15
8
0
1
2
00000000
10000000
15
0
8
7
  The ISA of our host machines in the lab (x86) and MIPS ISA that we will simulate both assume Little Endian

## Slide 11: Registers
Registers is a significantly faster (compared to memory) storage for data
    A great amount of registers are included into programmer-visible machine state (fully controlled by a programmer):
        Program counter stores the address of the currently executed instruction
        General Purpose Registers (GPR) is used to store intermediate calculations.
    The GPR can be thought as an array of elements indexed by numbers of registers encoded in instructions.
    The maximum number of the GRP is equal to , where N is the maximal number of bits that can be encoded in a instruction as a register number.

## Slide 12: Operations
Common types:
Set a register to constant value or value of other register (move operation).
Loads (memory → register ) & stores (register ← memory)
Read and write data from hardware devices (I/O) – not used in our project
Arithmetic and Logic:
    +, -, *, /, =. . .
    And, Or, Xor, Not
Compare two values of registers
Control flow (taking decision: loops, if-else)
  branch to another location (PC new value)
  conditionally branch (if (condition) then PC new value)
  save current location and jump to new location (Procedure call)

## Slide 13: MIPS Integer Arithmetic instruction format (R-type)
All MIPS instruction (not only R-Type) has fixed length of 4 Bytes
MIPS arithmetic instructions work only with registers.
The filed description:
  opcode denotes of the operation that is performed by this instruction
  rs stores register number of for the first source operand
  rt stores register number of for the second source operand
  rd stores register number where the result (destination operand) will be put
  shamt – used in shift instructions
  funct is a function code. It can slightly change the behavior of the operation encoded in opcode.
opcode
rs
rt
rd
shamt
funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits

## Slide 14: MIPS Integer Arithmetic instruction format (R-type)
opcode
rs
rt
rd
shamt
funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
add $t0, $s1, $s2
000000| 10001 | 10010 | 01000 | 00000 | 100000
opcode
rs
rt
rd
shamt
funct
add
$s1
$s2
$t0
signed
Example: encoding of
Due to Little Endian in the memory the bits of this instructions are “mirrored”:
IP
00000100
00000010
0
11
6
IP+1
IP+2
IP+3
…
…
01001100
21
01000000
26
31
Start address of the instruction
funct
shamt
rd
rt
rs
opcode
16

## Slide 15: Instruction Execution Cycle
Fetch Instruction by PC
Read registers
Process Calculations
Read/Write
Memory
Write registers
Update PC
Download instruction from the memory using value stored in the program counter (PC) register as an address.
Read values of registers which are pointed by the instruction as their source operands.
Execute an action encoded in the instruction (e.g. addition, subtraction, address calculation, etc.).
Write the result of the calculation into the memory or read the value using the address calculated on the previous step.
Write the result of the calculation or the value read on the previous step into the memory.
Update the program counter to the next instruction:
PC = PC + InstructionLength
Or it is a taken branch then:
PC = PC + InstructionLength + BranchOffset

## Slide 16: Acknowledgements
These slides contain material developed and copyright by:
Krste Asanovic (MIT/UCB), CS152-L1
David M. Koppelman (LSU), EE4720-L1

## Slide 17: Thank You