## Slide 1: Caches and Memory Hierarchy
Pavel Kryukov
03/01/2014

## Slide 2: Classic components of a computer
Computer
memory
processor
input
output
datapath
control

## Slide 3: CPU-Memory Performance Gap

## Slide 4: The city example (spatial locality)
Your shop
Factory
Shop store
Storehouse
Large storehouse
The delay is decreased, but the cost is increased

## Slide 5: The bookshelf example (temporal locality)
Places for books
Your table
City Library
fast
slow
Your bookshelf

## Slide 6: Full associative cache
Cache
Main memory
address
data
data
00000
01000
01001
10010
00101
address
00000
01001
01000
01100
10010
00101
10001
10000
01100
10001
10000

## Slide 7: A full associative cache scheme
V
Tag
Data
Data
30
32
=
Hit
Physical address tag
Byte offset
2
31 30 29 . . . . . . . . . . . . 12 11 10 9 8 . . . . . . 3 2 1 0
Address
V
Tag
Data
V
Tag
Data
V
Tag
Data
=
=
=
multiplexor
32
OR

## Slide 8: Direct mapped cache
001
010
011
000
100
101
110
111
00001
00101
01001
01101
10001
10101
Index length = log2(number of cache block)
Cache capacity is 8 = 23 , therefore the index takes 3 bites
Cache
Main memory
address
index
data
data

## Slide 9: Direct mapped cache scheme
0 |  |  | 
1 |  |  | 
2 |  |  | 
… |  |  | 
… |  |  | 
1022 |  |  | 
1023 |  |  | 
Valid
Tag
Data
Data
20
10
32
=
Cache hit
Index
Physical address tag
Cache index
Byte offset
2
31 30 29 . . . . . . . . . . . . 12 11 10 9 8 . . . . . . 3 2 1 0
Address

## Slide 10: Partial associativity
00
01
01
00
10
10
11
11
index
data
2
3
4
1
set
index
data
set
2
3
4
1
5
6
7
8
001
010
011
000
100
101
110
111
index
data
1
set
Not used
Fully associative cache
2-way set-associative
Direct mapped cache
The miss rate is decreased, but hit time, size, power are increased
Index length = log2(number of cache block/number of ways)

## Slide 11: A four-way set-associative cache
0 |  |  | 
1 |  |  | 
2 |  |  | 
… |  |  | 
… |  |  | 
254 |  |  | 
255 |  |  | 
V
Tag
Data
Data
22
8
32
=
Hit
Index
Physical address tag
Cache index
Byte offset
2
31 30 29 . . . . . . . . . . . . 12 11 10 9 8 . . . . . . 3 2 1 0
Address
V
Tag
Data
V
Tag
Data
V
Tag
Data
=
=
=
multiplexor
32
OR

## Slide 12: Associativity and bookshelf
A-B | C-D | E-F | G-H | I-J | … | … | … | … | Y-Z
Only one place for a book
Direct bookshelf
A-D |  | E-F |  | … |  | … |  | W-Z | 
Two-way set-associative bookshelf
Only two place for a book
Full associative bookshelf
Any place are available for a book

## Slide 13: Miss rate diagram
Compulsory misses. They are caused by the first reference to the data.
Capacity misses (due to cache capacity limitation only)
Conflict misses:
  Mapping misses (cache is not fully associative)
  Replacement misses (the replacement policy is not ideal)
Capacity misses
Conflict
Compulsory

## Slide 14: Cache Replacement
Direct map
  A new block is mapped to a single line in the cache
  Old line is evicted (re-written to memory if needed)
N-way set associative cache
  Choose a victim from all ways in the appropriate set
Replacement algorithms
  Optimal replacement algorithm
  FIFO – First In First Out
  Random
  LRU – Least Recently used
LRU is the best
  but not that much better even than random

## Slide 15: Writes handling
There is no write into the instruction cache.
In the most of modern systems the cache block is larger than store data, thus only the part of the cache block is updated.
Hit/miss logic is very similar to one in cache read.
Write request
Write the data into the cache block
Load block from the next level of hierarchy into the cache
Is tag equal?
Yes
No
Write hit
Locate block using index
Write miss

## Slide 16: Memory Update Policy on Writes
Write back
  “Store” operations that hit the cache write only to the cache
    Main memory is not accessed in case of write hit
    Line is marked as modified or dirty
  Modified cache line written to memory only when it is evicted
    Saves memory accesses when a line is updated many times
    On eviction, the entire line must be written to memory
      There is no indication which bytes within the line were modified
Write through
  Stores that hit the cache write both to cache and to memory
    Need to write only the bytes that were changed (not entire line)
  The ratio between reads and write is ~ 4:1
    While writing to memory, the processor goes on reading from cache
  No need to evict blocks from the cache (never dirty)
  Use write buffers so that don’t wait for lower level memory

## Slide 17: Write-through vs write-back
The key advantages of write-back:
  Individual words can be written by the processor at the rate that the cache, rather then the main memory, can accept them.
  Multiple writes within a block require only one write to the lower level in the hierarchy.
Ones of write-through:
  Evictions of a block from the cache are simpler and cheaper because they never require a block to be written back to the lower level of the memory hierarchy.
  Write-through is easier to implement than write-back

## Slide 18: Small summary

## Slide 19: Improving Cache Performance
Rates:
  Miss Rate = Misses / total CPU request
  Hit Rate = Hits / total CPU request = 1 – Miss Rate
Goal: reduce the Average Memory Access Time (AMAT):
  AMAT = Hit Rate * Hit Time + Miss Rate * Miss Penalty
  But HitRate ≈ 0.9, HitTime ≈ 10 clk, MissRate ≈ 0.1, MissPenalty ≈ 200 clk, then
  AMAT ≈ Hit Time + Miss Rate * Miss Penalty
Approaches:
  Reduce Hit Time
  Reduce Miss Penalty
  Reduce Miss Rate
Notes:
  There may be conflicting goals
  Keep track of clock cycle time, area, and power consumption
Cache
ALU
Hit Time =
Memory
Hit!
(ALU to Cache Transfer)
+ (Hit/Miss check)
+ (Cache to ALU)

## Slide 20: Improving Cache Performance
Rates:
  Miss Rate = Misses / total CPU request
  Hit Rate = Hits / total CPU request = 1 – Miss Rate
Goal: reduce the Average Memory Access Time (AMAT):
  AMAT = Hit Rate * Hit Time + Miss Rate * Miss Penalty
  But HitRate ≈ 0.9, HitTime ≈ 10 clk, MissRate ≈ 0.1, MissPenalty ≈ 200 clk, then
  AMAT ≈ Hit Time + Miss Rate * Miss Penalty
Approaches:
  Reduce Hit Time
  Reduce Miss Penalty
  Reduce Miss Rate
Notes:
  There may be conflicting goals
  Keep track of clock cycle time, area, and power consumption
Cache
ALU
Miss Penalty =
Memory
Miss!
(ALU to Cache Transfer)
+ (Hit/Miss check)
+ (Cache to Memory)
+ (Memory Search)
+ (Memory to Cache)
+ (Cache to ALU)

## Slide 21: Tuning Basic Cache Parameters: Size, Associativity, Block width
Size:
  Must be large enough to fit working set (temporal locality)
  If too big, then hit time degrades
Associativity:
  Need large to avoid conflicts, but 4-8 way is as good as FA (full associative)
  If too big, then hit time degrades
Block:
  Need large to exploit spatial locality & reduce tag overhead
  If too large => cache has few blocks => higher miss rate & miss penalty
Size
Associatively
Block width
Hit rate
≈4

## Slide 22: Multilevel caches
Motivation:
  Optimize each cache for different constraints
  Exploit cost/capacity trade-offs at different levels
L1 caches
  Optimized for fast access time (1-3 CPU cycles)
  8KB-64KB, DM to 4-way SA
L2 caches
  Optimized for low miss rate (off-chip latency high)
  256KB-4MB, 4- to 16-way SA
L3 caches
  Optimized for low miss rate (DRAM latency high)
  Multi-MB, highly associative
Processor
L1-instr
L1-data
L2-cache
L3-cache
AMD Opteron

## Slide 23: 2-level Cache Performance Equations
L1 AMAT = HitTimeL1 + MissRateL1 * MissPenaltyL1
  MissLatencyL1 is low, so optimize HitTimeL1
MissPenaltyL1 = HitTimeL2 + MissRateL2 * MissPenaltyL2
  MissLatencyL2 is high, so optimize MissRateL2
  MissPenaltyL2 = DRAMaccessTime + (BlockSize/Bandwidth)
  If DRAM time high or bandwidth high, use larger block size
L2 miss rate:
  Global: L2 misses / total CPU references
  Local: L2 misses / CPU references that miss in L1
  The equation above assumes local miss rate
L1-Cache
ALU
L2-Cache
HitTimeL1
HitTimeL2
BlockSize/Bandwidth
DRAM
DRAMaccessTime is time to find block in DRAM
Bandwidth – how many bytes can be transacted from DRAM per cycle

## Slide 24: Improvement of AMAT for 2-level system

## Slide 25: Reduce Cache Hit Time
Techniques we have seen so far (most interesting for L1)
  Smaller capacity
  Smaller associativity
Additional techniques
  Wide cache interfaces
  Pseudo-associativity
Techniques that increase cache bandwidth (number of concurrent accesses)
  Pipelined caches
  Multi-ported caches
  Multi-banked caches

## Slide 26: Reduce Miss Rate
Techniques we have already seen before
  Larger caches
    Reduces capacity misses
  Higher associativity
    Reduces conflict misses
  Larger block sizes
    Reduces cold misses
Additional techniques
  Skew associative caches
  Victim caches

## Slide 27: Victim Cache
Small FA cache for blocks recently evicted from L1
  Accessed on a miss in parallel or before the lower level
  Typical size: 4 to 16 blocks (fast)
Benefits
  Captures common conflicts due to low associativity or ineffective replacement policy
  Avoids lower level access
Notes
  Helps the most with small or low-associativity caches
  Helps more with large blocks
Cache
Victim
Cache
Lower level

## Slide 28: Reducing Miss Penalty
Techniques we have already seen before:
  Multi-level caches
Additional techniques
  Sub-blocks
  Critical word first
  Write buffers
  Non-blocking caches

## Slide 29: Sub-blocks
Idea: break cache line into sub-blocks with separate valid bits
  But the still share a single tag
Low miss latency for loads:
  Fetch required subblock only
Low latency for stores:
  Do not fetch the cache line on the miss
  Write only the sub-block produced, the rest are invalid
  If there is temporal locality in writes, this can save many refills

## Slide 30: Write buffers
Write buffers allow for a large number of optimizations
Write through caches
  Stores don’t have to wait for lower level latency
  Stall store only when buffer is full
Write back caches
  Fetch new block before writing back evicted block
CPUs and caches in general
  Allow younger loads to bypass older stores
Cache L1/Cache L2
CPU/Cache L1
stores