## Slide 1: MIPT-MIPS 2013 Advanced Pipelining: Complex and Superscalar Pipelines
Alexander Titov
22.03.2014

## Slide 2: Unified Pipeline
So far only a unified pipeline have been considered where each instruction takes the same number of cycles to execute
Why?
R1 ← MEM[Addr]
...
R1 ← R2 + R3
Latencies
4 cycles
…
1 cycle
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |  | 
F | D | E | M |  |  | W |  |  |  |  | 
 | F | D | … |  |  |  |  |  |  |  | 
 |  | F | D | E | W |  |  |  |  |  | 
The real latency of instructions can differ significantly:
  Memory systems with variable access time
  Long latency or non/partially pipelined floating-point units
– In order to prevent out-of-order instruction completion, which may lead to writing wrong register value:
The add writes R1 before the load, i.e. the next instruction will consume the wrong value of R1

## Slide 3: Disadvantages of Long Unified Pipelines
Unified Pipeline resolves the problem with out-of-order completion, but has a problem with bypasses if the number of stage is large
F | D | E |  |  |  |  | W |  | 
 | F | D | E | … |  |  |  |  | 
 |  | F | D | E | … |  |  |  | 
 |  |  | F | D | E | … |  |  | 
 |  |  |  | F | D | E | … |  | 
 |  |  |  |  | F | D | E | … | 
 |  |  |  |  |  | F | D | E | …
 |  |  |  |  |  |  | F | D | E
The more stages have been added to make writeback in-order the more bypasses are needed.
It makes bypass multiplexor too huge and slow
Only this instruction can safely read its sources from the Register File
Unfeasible bypasses (too many stage to take a value from) makes the concept of a unified pipeline inefficient
  Full bypasses are too huge to be implemented in real hardware and too slow → significantly increase the clock time
  Without full bypasses there will be bubbles in the pipeline → low CPI

## Slide 4: Complex Pipeline
Decision is using non-unified (i.e., complex) pipeline, but fix somehow the problem with out-of-order completion
Need track not only true dependences, but also Write-After-Write (WAW) ones:
Code Example:
1. R1 ← MEM[Addr]
2. R4 ← R1 * R3
3. R1 ← R2 + R3
True dependence (Read-After-Write)
False dependence (Write-After-Write)
1. R1 ← MEM[Addr]
2. R4 ← R1 * R3
1. R1 ← MEM[Addr]
3. R1 ← R2 + R3
Anti-dependence (Write-After-Read)
2. R4 ← R1 * R3
3. R1 ← R2 + R3
Not a problem for now, as instruction cannot write the results until all the previous read their sources either from the RF or bypasses
Not a problem for now, as all instruction are issued in-order:
the result is in the RF or available through bypass
Need to obey this kind of dependencies

## Slide 5: Example of Complex Pipeline
F | D | I | E | W |  |  |  | 
 |  |  | E | Mem1 | Mem1 | … | W | 
 |  |  | Mul1 | Mul2 | Mul3 | W |  | 
 |  |  | Div1 | Div2 | Div3 | Div4 | Div5 | W
Issue is a new stage responsible for analyzing WaW dependencies and resource conflict on writeback
To prevent violation of WaW or writeback conflict an instruction that causes it is stalled on this stage

## Slide 6: Scoreboard for tracking WAW
The solution is “book-keeping” on the issue stage (so-called scoreboarding)
  Know everything: weather a register is being calculated or available in the RF/Bypass, when it will be ready, which unit processes it, etc.
 | 5 | 4 | 3 | 2 | 1 | In Bypass | In RF
R1 |  |  |  |  |  |  | 
R2 |  |  |  |  |  |  | 
R3 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
R32 |  |  |  |  |  |  | 
1
1
1
1
Number of cycles till writeback
on writeback?
in RF?
On issue stage check the table:
  Check WaW
    There is no operation that will write the same register later than the current instruction
  Check resource conflict on WriteBack
    There is no operation that will write any register in the same cycle
  If all conditions are satisfied:
    Update the table by information on the destination
    Go to the next stage
  If not – stall the instruction
Shift all “1” left every cycle
Example of a scoreboard table:
Algorithm:

## Slide 7: Next details
The rest part of the presentation was presented using a blackboard:
  Exception/Interrupt processing (ROB + ARF)
  Bypassing

## Slide 8: Thank You Q/A

## Slide 9: Ordering for Exceptions/Interrupts
Scorebord allows to track WaW dependencies and enables the complex pipeline, however it break the original order
  Can the instruction #2 write earlier than #1?
  If it does that the program will not be broken, because there is no dependencies between this instructions
1. R1 ← MEM[Addr]
2. R2 ← R2 + R3