## Slide 1: Pipelining (part II)
Alexander Titov
6 December 2014

## Slide 2: Refresher: Pipelined vs. Non-Pipelined MIPS
F
D
E
M
W
PC
F
D
E
M
W
PC + 4
F
D
E
M
PC + 8
instructions
time
Sync signal
(clocks)
4ns
8ns
12ns
16ns
wait
F
D
E
M
W
wait
PC
PC + 4
PC + 8
wait
F
D
E
M
W
wait
wait
F
D
E
M
W
wait
time
Sync signal
(clocks)
4ns
8ns
12ns
16ns
Pipelined
Non-Pipelined

## Slide 3: Refresher: Forwarding + Hazard Detection Unit
Control
EX
M
WB
Forwarding
Unit
1
m
u
x
0
0
m
u
x
1
0
m
u
x
1
2
0
m
u
x
1
2
Data
Memory
ALU
Register
File
Instruction
Memory
PC
ID/EX
EX/MEM
MEM/WB
IF/ID
Instruction
IF/ID.Rs
IF/ID.Rt
IF/ID.Rt
IF/ID.Rd
Rs
Rt
Rt
Rd
WB
M
WB
EX/MEM.Rd
MEM/WB.Rd
Hazard
Detection
Unit
0
ID/EX.MemRead
PC Write
0
m
u
x
1
IF/ID Write
ID/EX.Rt

## Slide 4
Executing a BEQ Instruction (1)
beq R4, R5, 27;
0 or
4 beq R4, R5, 27 8 and 12 sw
16 sub
ALUSrc
6
ALU
result
Zero
Add
result
Add
Shift
left 2
ALU
Control
ALUOp
RegDst
RegWrite
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
MemRead
MemWrite
Address
Write
Data
Read
Data
Data
Memory
Branch
PCSrc
MemtoReg
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
R4
R5
27
8
beq
12
12
and
Calculate branch condition
-
Calculate branch target
# if(R4 - R5 == 0)
# then PC (PC + 4) + SignExt(27)*4;
# else PC  PC+4

## Slide 5
Executing a BEQ Instruction (2)
beq R4, R5, 27;
0 or
4 beq R4, R5, 27 8 and 12 sw
16 sub
# if(R4 - R5 == 0)
# then PC (PC + 4) + SignExt(27)*4;
# else PC  PC+4
ALUSrc
6
ALU
result
Zero
Add
result
Add
Shift
left 2
ALU
Control
ALUOp
RegDst
RegWrite
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
MemRead
MemWrite
Address
Write
Data
Read
Data
Data
Memory
Branch
PCSrc
MemtoReg
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
R4-R5=0
-
8+SignExt(27)*4
12
16
16
beq
and
sw

## Slide 6
Executing a BEQ Instruction (3)
beq R4, R5, 27;
0 or
4 beq R4, R5, 27 8 and 12 sw
16 sub
# if(R4 - R5 == 0)
# then PC (PC + 4) + SignExt(27)*4;
# else PC  PC+4
ALUSrc
6
ALU
result
Zero
Add
result
Add
Shift
left 2
ALU
Control
ALUOp
RegDst
RegWrite
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
MemRead
MemWrite
Address
Write
Data
Read
Data
Data
Memory
Branch
PCSrc
MemtoReg
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
16
20 or 116
beq
and
sw
20
sub
  If the branch is taken the 3 wrong instructions get into the pipeline (they must be canceled somehow)
  => We are loosing 3 cycles after each taken branch!

## Slide 7
Decision 1: Always Fetch Not Taken
Execute instructions from the fall-through (not-taken) path as if there is no branch
If the branch is not-taken (~50%), no penalty is paid
If branch actually taken:
  Flush the fall-through path instructions before they change the machine state (memory / registers)
  Fetch the instructions from the correct (taken) path
Assuming ~50% branches not taken on average. How lower it will be that ideal pipeline?
CPI ideal (Clock per instruction) =
CPI real =
CPI ideal +
(% of branches × 0.5)
× Penalty =
1.3
~20%
3
1
  30% slower => need to find something better

## Slide 8
Decision 2: Delayed Branches
Maybe ask the software (SW) to help?
  Need to change ISA to give it such possibility
Define branch to take place AFTER n following instructions
  Hardware (HW) executes n instructions following the branch regardless of branch is taken or not
SW puts in the n slots following the branch instructions that can be executed regardless of branch resolution
  Instructions that are before the branch instruction, or
  Instructions from the converged path after the branch
If cannot find independent instructions, put NOPs
Not Taken path
Taken path
Converged path
Branch
Only if it doesn’t depend on the instructions in T and NT paths
Only if it doesn’t define the branch condition

## Slide 9
Decision 2: Delayed Branches
Unfortunately, filling 1 delay slot is easy, 2 is hard, 3 is harder …
  Assuming we can effectively fill d% of the delayed slots
  CPI real = 1 + 0.2 × (3 × (1-d))
  For example, for d=0.6, we get CPI real = 1.2
Mixing architecture with micro-arch
  New generations requires more delay slots
  Cause computability issues between generations
  Still far from the ideal and mixing Arch and uArch is almost always not the best decision.
  Can we do something even better?

## Slide 10
Decision 3: Dynamic prediction
Dynamic branch prediction approach:
  As soon as branch is fetched (at IF stage) change the PC to the predicted path.
  Switch to the right path after the branch execution if the prediction was wrong.
It required complex hardware at IF stage that will predicts:
  Whether the instruction is a branch
  Branch taken or not
  Taken branch target
Structure performs such function is called Branch Target Buffer (BTB)
  In fact, it is organized exactly as a cache

## Slide 11
In case of correct prediction – loose nothing
In case of wrong prediction – flush the pipeline and restart from the correct PC
  Wrong prediction cases
    Predict not-taken, actual taken
    Predict taken, actual not-taken, or actual taken but wrong target
Assuming P% correct prediction rate
CPI real = 1 + (0.2 × (1-P)) × 3
  For example, if P=0.85 (the modern predictors has > 0.95)
CPI real = 1 + (0.2 × 0.15) × 3 = 1.09
Performance of Dynamic Prediction

## Slide 12
Allocation
  Allocate instructions identified as branches (after decode)
    Both conditional and unconditional branches are allocated
  Not taken branches need not be allocated
    BTB miss implicitly predicts not-taken
Prediction
  BTB lookup is done parallel to IC lookup
  BTB provides
    Indication that the instruction is a branch (BTB hits)
    Branch predicted target
    Branch predicted direction
    Branch predicted type (e.g., conditional, unconditional)
Update (when branch outcome is known)
  Branch target
  Branch history (taken / not-taken)
BTB functions

## Slide 13
Wrong prediction cases
  Predict not-taken, actual taken
  Predict taken, actual not-taken, or actual taken but wrong target
In case of wrong prediction – flush the pipeline
  Reset latches (same as making all instructions to be NOPs)
  Select the PC source to be from the correct path
    Need get the fall-through with the branch
  Start fetching instruction from correct path
Assuming P% correct prediction rate
CPI real = 1 + (0.2 × (1-P)) × 3
  For example, if P=0.85 (the modern predictors has > 0.95)
CPI real = 1 + (0.2 × 0.15) × 3 = 1.09
BTB functions

## Slide 14
A saturating counter or bimodal predictor is a state machine with four states:
Why four states?
  Bimodal predictor make only one mistake on a loop back branch (on the loop exit)
Advantages:
  Small – only 2 bits per entry in the BTB
  Predicts well branches with stable behaviour
Disadvantages
  Cannot predict well branches which often change their outcome:
    e.g. T, NT, T, NT, T, NT, T, NT, T, …
How to predict branch outcome?

## Slide 15
1 0 0 1 0 0 1 0 0
0 0 0 0 0 1 0 0 0
Two-level adaptive predictor
past
future
present
History buffer
weakly
NT
strongly
NT
strongly
T
weakly
T
00
weakly
NT
strongly
NT
strongly
T
weakly
T
01
weakly
NT
strongly
NT
strongly
T
weakly
T
10
weakly
NT
strongly
NT
strongly
T
weakly
T
11
Prediction:
TRUE
Result:
FALSE
Pattern history table
Branch sequence:

## Slide 16
Using The BTB
PC moves to next instruction
Br taken ?
BTB Hit ?
Inst Mem gets PC
and fetches new inst
BTB gets PC
and looks it up
IF/ID latch loaded
with new inst
IF
ID
IF/ID latch loaded
with pred inst
IF/ID latch loaded
with seq. inst
yes
PC  PC + 4
no
no
PC  perd addr
yes
Branch ?
no
yes
EXE

## Slide 17
MEM
WB
Flush pipe &
update PC
no
IF/ID latch loaded
with correct inst
yes
continue
continue
Corect
pred ?
Calculate br
cond & trgt
ID
EXE
Branch ?
yes
no
Using The BTB
Update BTB

## Slide 18
Adding a BTB to the Pipeline
Shift
left 2
ALUSrc
6
ALU
result
Zero
+
ALU
Control
ALUOp
RegDst
RegWrite
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM
/WB
Instruction
MemRead
MemWrite
Address
Write
Data
Read
Data
Data
Memory
Branch
PCSrc
MemtoReg
4
+
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
m
u
x
1
0
m
u
x
Inst.
Memory
Address
Instruction
BTB
1
2
pred target
pred dir
PC+4 (Not-taken target)
taken target
3
Mis-
predict
Detection
Unit
Flush
predicted target
PC+4 (Not-taken target)
predicted direction
−
4
address
target
direction
alloc/updt

## Slide 19: Acknowledgments
These slides contain material developed and copyright by:
Lihu Rappoport (MAMAS/Intel), 234267, L2