## Slide 1: Advanced Pipelining
Alexander Titov
13 December 2014

## Slide 2: Unified Pipeline
So far only a unified pipeline have been considered where each instruction takes the same number of cycles to execute
The real latency of instructions can differ significantly:
  Memory systems with variable access time
  Long latency calculations (multiplication, division, floating point operations, etc.)
Increasing of the clock cycle to fit the longest instruction and thereby keeping pipeline unified may be inefficient
wait
F
wait
W
D
wait
E longest
M
wait
E medium
E short
Most of instructions are shorter and do not need such long clock cycle
Sync signal
(clocks)
time
4ns
8ns
12ns
16ns
20ns

## Slide 3: Unified Pipeline
The problem is resolved by splitting execution into more stages
F | D | E1 | E2 | E3 | E4 | M | W | 
F | D | E1 | E2 | E3 | E4 | M | W |  | 
 | F | D | E1 | … |  |  |  |  | 
 |  | F | D | E1 | … |  |  |  | 
 |  |  | F | D | E1 | … |  |  | 
 |  |  |  | F | D | E1 | … |  | 
 |  |  |  |  | F | D | E1 | … | 
 |  |  |  |  |  | F | D | E1 | …
 |  |  |  |  |  |  | F | D | E1
F |  |  |  | D |  |  |  | E longest | M |  |  |  | W |  |  | 
F | D | E1 | E2 | E3 | E4 | M | W | 
But, for better overlapping of short instructions a complicated forwarding is required (too many stage to take a value from)
Unfeasible makes the concept of a unified pipeline inefficient
  Full forwarding are too huge and slow → increase the clock cycle
  Without full forwarding there will be bubbles in the pipeline → high CPI
Only this instruction can safely read its sources from the Register File

## Slide 4: Non-Unified Pipeline
Ok, let’s make non-unified pipeline
R1 ← R2 / R3
...
R1 ← R2 + R3
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |  | 
F | D | E1 | E2 | E3 | E4 | W |  |  |  |  | 
 | F | D | … |  |  |  |  |  |  |  | 
 |  | F | D | E1 | W |  |  |  |  |  | 
– Yes, out-of-order instruction completion, which may lead to writing wrong register value
The add writes R1 before the division, i.e. the next instruction will consume the wrong value of R1
F | D | E1 | M | W | 
F | D | E1 | E2 | E3 | E4 | W | 
F | D | E1 | E2 | W | 
Any problems?
F | D | E1 | W | 
Simple arithmetic
Memory accesses
Complex arithmetic
Floating point arith.

## Slide 5: Complex Pipeline
Decision is using non-unified (i.e., complex) pipeline, but fix somehow the problem with out-of-order completion
Need track not only true dependences, but also Write-After-Write (WAW) ones:
Code Example:
1. R1 ← MEM[Addr]
2. R4 ← R1 * R3
3. R1 ← R2 + R3
True dependence (Read-After-Write)
False dependence (Write-After-Write)
1. R1 ← MEM[Addr]
2. R4 ← R1 * R3
1. R1 ← MEM[Addr]
3. R1 ← R2 + R3
Anti-dependence (Write-After-Read)
2. R4 ← R1 * R3
3. R1 ← R2 + R3
Not a problem for now, as instruction cannot write the results until all the previous read their sources either from the RF or bypasses
Not a problem for now, as all instruction are issued in-order:
the result is in the RF or available through bypass
Need to obey this kind of dependencies

## Slide 6: Scoreboard for tracking WAW
The solution is “book-keeping” on the issue stage (so-called scoreboarding)
  Know everything: weather a register is being calculated or available in the RF/Bypass, when it will be ready, which unit processes it, etc.
 | 5 | 4 | 3 | 2 | 1 | In Bypass | In RF
R0 |  |  |  |  |  |  | 
R1 |  |  |  |  |  |  | 
R2 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
R31 |  |  |  |  |  |  | 
1
1
1
1
Number of cycles till writeback
on writeback?
in RF?
On issue stage check the table:
  Check WaW
    There is no operation that will write the same register later than the current instruction
  Check resource conflict on WriteBack
    There is no operation that will write any register in the same cycle
  If all conditions are satisfied:
    Update the table by information on the destination
    Go to the next stage
  If not – stall the instruction
Shift all “1” right every cycle
Example of a scoreboard table:
Algorithm:

## Slide 7: Thank You Q/A