## Slide 1: Out-Of-Order Execution (part III)
Alexander Titov
11 April 2015

## Slide 2: Refresher: Memory Dependencies
Instructions can be dependent through memory
  So far we consider only dependency through register
They cannot be checked at allocation
  Need to calculate addresses of the load and all stores
Straightforward solution: a load waits until all previous stores write to memory/cache
  As stores write only after their retirement, it postpones execution of a load almost to its retirement
  Unlike stores, loads are waiting by many other instruction
It is too slow → need to find a better solution
    (1) Mem[r2]  …
    …
    (6) …  Mem[r3]
  If memory space written by (1) is overlapped with one read by (6) then there is dependency.
  In this case, (6) cannot be executed before (1)

## Slide 3: Load and Store Buffer
Improvement: load does not wait if there is no overlapping
  Need to wait until all previous stores calculate their address
  Then, check for overlapping
  Fast case: no overlapping → load waits nothing
  Slow case: overlapping → load waits until the closest overlapping store update memory/cache
Store can be at any ROB entry → any entry should be checkable
  To large and slow HW
  On the other hand, not every instruction is load or store
  Like SQ, we can use smaller buffers for stores and loads only (store buffer or SB and load buffer or LB)
  All complex check of the address are done in LB and SB
  ROB just keeps the order of instructions

## Slide 4: SB and LB Operation
(5) …  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready?
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
… |  |  |  | 
M |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
(5) …  Mem[r5]
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
oldest unknown
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x25]
[0x01]
[0x25]
[0x35]
[0x35]
[0x25]
OK
yes
[0x35]
NO: (1)
0

## Slide 5: Store Forwarding
Why does load wait for the store retirement in case of overlapping?..
Improvement: load can take data of the overlapping store
It is called Store Forwarding
  Only for simplicity

## Slide 6: False Dependency from Store Data
If there is no overlapping load does not depend on store data
It depends only on store address
  To know that there is no overlapping load wait until all store addresses are calculated
Address is calculated when store is executed
But, store is sent to execution only all its sources (including data) are ready → there is a false dependency from data
(1) r1  …
(2) r2  …
(3) Mem[r1]  r2
…
(N) …  Mem[r3]
1
2
3
N
r1
r2
address
Example:
Data Flow Graph
  r3 != r1 → (3) and (N) are not overlapped
  False dependency:
  in fact, (N) does not need to wait (2)

## Slide 7: STA and STD
To remove false dependency in case of absence of overlapping store instruction is executed in two steps:
  Store address calculation (STA)
  Store data calculation (STD)
Load is waiting for STD only if it overlapped with STA
(1) r1  …
(2) r2  …
(3) addr  [r1]
(3’) Mem[addr]  r2
…
(N) …  Mem[r3]
1
3
N
r1
addr
Example:
Data Flow Graph
  Exist only if overlapping is detected
STA →
STD →
2
r2
3’
data

## Slide 8: SB and LB Operation: STA and STD
(5) …  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready?
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
… |  |  |  | 
M |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
(5) …  Mem[r5]
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
oldest unknown
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x25]
[0x01]
[0x25]
[0x35]
[0x35]
[0x25]
yes
[0x35]
0
Data
data: 0x100
0x100
(1)
yes
hit

## Slide 9: End of Part I