## Slide 1: Pipeline Modeling
Pavel Kryukov
13 December 2014

## Slide 2: Refresher: MIPS Single-Cycle Implementation
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
CondCode
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 2
Add
Add
PC
4
0
1
m
u
x
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
RegWrite
ALUop
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
Control
CondCode
Fetch
Decode
Execute
Memory
WriteBack
F
D
E
M
W
2ns
1ns
2ns
2ns
1ns
Fig.: the MIPS main stages
We are not going to model each component (e.g. multiplexer, adder) as it is done in RTL simulator

## Slide 3: Single-Cycle Implementation modeling
void MIPS::run(const string& tr) {
// ... load trace
this->PC = startPC;
for (uint i = 0; i < instr_to_run; ++i) {
uint32 bytes = fetch(); // fetch() { return mem->read(PC); }
FuncInstr instr(bytes);
read_src(instr); // read_src() { instr->v_src1 = rf->read(instr->rs); …}
instr->execute(); // execute_add() { v_dst = v_src1 + v_src2; }
ld_st(instr);
wb(instr); // wb() { rf->write(instr->rd, instr->v_dst); }
PC = update_pc(instr);
}
F
D
E
M
W
class MIPS {
// storages of internal state
RF* rf;
uint32 PC;
Memory* mem;
void ld_st(FuncInstr& inst);
void wb(const FuncInstr& inst);
public:
MIPS();
void run(const string&, uint instr_to_run);
};

## Slide 4: Performance modeling
In single-cycled MIPS every instruction is executed in 1 cycle
To get pipelined MIPS performance, we have to model timing of each pipeline stage of instruction due to stalls
In HW, pipeline stages are divided by latches that are updated every cycle.
Modeling of latch is possible, but its interface is complicated The more convenient solution is called ports

## Slide 5: Ports
From interface port of view, one port consists of two parts, implemented in classes ReadPort and WritePort.
class Module1 {
WritePort<uint>* wp;
Module1() {
wp = new WritePort<uint>(“DATA_PORT”);
wp->set_bandwidth(1);
}
};
class Module2 {
ReadPort<uint>* rp;
Module2() {
rp = new ReadPort<uint>(“DATA_PORT”);
rp->set_latency(5);
}
};
Ports are connected by equal string key
Module1::do_action(uint64 cycle) {
// …
wp->write(data, cycle);
}
// this method must be run every cycle!
Module2::clock(uint64 cycle)
uint data;
while (rp->read(&data, cycle)) {
// …
}
}
Imagine that here we following functions:
wp->write(8, 0);
wp->write(9, 2);
Let’s look how it will be executed here:
rp->read(&data, 0); // data is trash, returns false
rp->read(&data, 1); // data is trash, returns false
rp->read(&data, 2); // data is trash, returns false
rp->read(&data, 3); // data is trash, returns false
rp->read(&data, 4); // data is trash, returns false
rp->read(&data, 5); // data is 8, returns true!
rp->read(&data, 6); // data is trash, returns false
rp->read(&data, 7); // data is 9, returns true!

## Slide 6: Example: decoder
Decoder::clock(uint64 cyc) {
while (rp_fetch_to_decoder->read(&this->dec_bytes, cyc) {
this->instr = FuncInstr(this->dec_bytes);
}
read_src(this->instr);
if (this->instr.srcs_ready)
wp_decoder_to_execute->write(instr, cyc);
else
wp_decoder_to_fetch->stall(true, cyc);
}
Executor::clock(uint64 cyc) {
FuncInstr instr;
while (rp_decoder_to_execute->read(&exec_instr, cyc) {
instr->execute();
// … to ldst and writeback
}
}
MIPS::clock(uint64 cyc) {
this->decoder->clock(cyc);
this->executor->clock(cyc);
}

## Slide 7: Extra reading
Asim: A Performance Model Framework http://www.ckluk.org/ck/papers/asim_ieeecomputer.pdf
Manual on MIPT-MIPS Ports https://code.google.com/p/mipt-mips/wiki/CommunicationBetweenModulesThroughPorts

## Slide 8: Thank You