## Slide 1: Boolean Algebra Combinational Circuits
Pavel Kryukov 10 October 2015

## Slide 2: Layers of Abstraction in Computes Science
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture
Less about physics, wires and transistors…
More about logical circuits

## Slide 3: Abstracting From Physics
Real physical circuits deal with physical properties, such as voltages and currents
Digital circuits use the abstractions of 0 and 1 to represent the presence or absence of these physical properties (signals) rather than a continuous range
Logic 1
Logic 0
Weak 1
Weak 0
undefined
5 V
3.5 V
1.5 V
0 V
voltage
It could not be a stable state: should not occur in the circuit except during transitions from one state to he other
Boolean algebra describes two-stated systems

## Slide 4: Boolean Algebra

## Slide 5: Boolean Algebra
Boolean Algebra (BA) works with object that can take only two values (true and false, or 1 and 0)
    Such object is called a Boolean object (term bit of information is used in CS)
    BA defines operations on Boolean objects → Boolean operations and functions
    It is convenient to represent these operations and functions via truth tables:
a | b | c
c = F(a,b)
b
a
c
Boolean function
Truth table
a | b | c
0 | 0 | 
a | b | c
0 | 0 | c00
a | b | c
0 | 0 | c00
0 | 1 | c01
1 | 0 | c10
1 | 1 | c11
George Boole
(1815 – 1864)
English mathematician, philosopher and logician

## Slide 6: Main Boolean operations
The simplest Boolean operation is …
AND (or Boolean multiplication)
  AND is often used as a logical key:
inversion (NOT)
x
!x
x | !x
0 | 1
1 | 0
x*y
x
y
x | y | x*y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
0
0
1
x | y | x*y
0 (closed) | y | 0
1 (open) | y | y

## Slide 7: Main Boolean operations
OR (or Boolean addition)
x+y
x
y
x | y | x+y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
1
XOR (or exclusive OR, or addition by module 1)
x | y | x  y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
0
x  y
x
y
= x*!y + !x*y

## Slide 8: Main axioms
There about ten axioms and theorems that can be used to create new or to simplify existed functions
Axiom | AND form | OR form
Identity law | 1*x = x | 0 + x = x
Idempotent law | x*x = x | x + x = x
Inverse law | !x*x = 0 | !x + x = 1
Commutative law | xy = yx | x + y = y + x
Associative law | (xy)z = x(yz) | (x + y) + z = x + (y + z)
Distributive law | xy + z = (x + z)(y + z) | (x + y)z = xz + yz
De Morgan's laws | !(xy) = !x + !y | !(x + y) = !x!y
… and a lot of other useful equations:
!(!x + y) + !(!x + !y) = x
(Huntington equation)

## Slide 9: Boolean functions
Boolean operations can be combined into functions
F(x, y, z) = x + !y*z
x
y
z
x + !y*z
x | y | z | F
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | … | … | 1
0
1
0
0

## Slide 10: Examples of reduction
F = (!x!y!z) + (!x y z) + (x !y !z) + (x y !z) =
= (!x !y !z) + (!x y z) + (x !z)(!y + y) =
= (!x !y !z) + (!x y z) + (x !z) =
= !x (!y !z + y z) + (x !z) =
= !x (!y  z) + (x !z).
= (!x + x)(!y !z) + (!x y z) + (x y !z) =
= (!y!z) + y(!x z + x !z) =
= (!y!z) + y(x  z) =
= !(y + z) + y(x  z).

## Slide 11: Canonical disjunctive normal form (CDNF)
CDNF is an algorithm of reconstructing a Boolean function from its truth table
    Take lines with ‘1’ only
    Conjunct all variables in line with correct sign
    Make disjunction on expressions
x | y | z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
!x * !y * !z
!x * y * z
x * !y * !z
x * y * !z
F = (!x!y!z) + (!x y z) + (x !y !z) + (x y !z)

## Slide 12: Canonical conjunctive normal form (CCNF)
CCNF is an algorithm of reconstructing a Boolean function from its truth table
    Take lines with ‘0’ only
    Make disjunction on all variables in line with correct sign
    Conjunct expressions
x | y | z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
x + y + !z
x + !y + z
!x + y + !z
!x + !y + !z
F = (x + y + !z)(x + !y + z)(!x + y + !z)(!x + !y + !z)

## Slide 13: Combinational Circuits

## Slide 14: Combinational Circuits
If the output of a function is completely defined by the current input then the function is called combinational :
Qt = F(xt, yt, zt, …)
Combinational circuit (scheme) is an implementation of a combinational function
A lot of things can be implemented using combinational circuits
    Just a few examples that will be presented soon: adder, decoder, multiplexer

## Slide 15: Many-input devices
Primitives like OR, AND may be composed to support several inputs
x+y
x
y
z
w
z+w
x+y+z+w
x
y
z
w
x+y+z+w

## Slide 16: Binary Decoder
A0 | A1 | D0 | D1 | D2 | D3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
A binary decoder is a logic circuit that converts a binary integer value to an associated pattern of output bits.

## Slide 17: Multiplexer
A multiplexer (or mux) is a device that selects one signals and forwards the selected input into a single line.
The entry wires are address bus and data buses
Address bus is connected via decoder
A0 | A1 | Out
0 | 0 | M0
0 | 1 | M1
1 | 0 | M2
1 | 1 | M3
M0
M1
M2
M3
A0
A1
Out

## Slide 18: Comparator
A comparator is a device that takes two numbers as input in binary form and determines whether one number is greater than, less than or equal to the other number
EQ
LEQ
 | EQ | LEQ
A>B | 0 | 0
A=B | 1 | 1
A<B | 0 | 1

## Slide 19: Adder and ALU

## Slide 20: Half adder scheme
half +
y
x
sum
carry
It is an adder, but it is not a full adder, because it does not have input carry
x | y | s | c
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0
1
1
0
0
0
0
1
Calculations:
It is an adder, but it is not a full adder, because it does not have input carry
Sum =
= !x * y + x * !y =
= x  y
Carry = x * y
x
y
s
c

## Slide 21: Full adder scheme
half +
yn
xn
cn-1
half +
sn
Cn
0 | 0 | 1 |  | 
0 | 1 | 1 |  | 
1 | 0 | 1 |  | 
1 | 1 | 1 |  | 
1
0
0
1
0
1
1
1
It is called a full adder
+
y
x
sum
carry
c
xn | yn | cn-1 | sn | cn
0 | 0 | 0 |  | 
0 | 1 | 0 |  | 
1 | 0 | 0 |  | 
1 | 1 | 0 |  | 
0
1
1
0
0
0
0
1
We add input carry here

## Slide 22: Wide adder
+
yn
xn
+
yn+1
xn+1
cn-1
cn
cn+1
sn
sn+1
+
+
+
We may add more adders to sum numbers wider than 1 bit
In real HW, wide adders have more complicated schemes to avoid long “carry chains”

## Slide 23: Arithmetic Logic Unit
ALU is a circuit that is able to perform different arithmetic and bitwise logical operations on integer binary numbers
ALU
Operand 1 (X)
Operand 2 (Y)
Opcode (I)
Result (out)

## Slide 24: Thank You